## Slide 1
IBM Internship · Research Project · 2026
Autonomous Vehicle &
Object Detection System
A unified real-time perception pipeline: Object Detection · 3D BEV · Lane Detection · Depth Estimation
Powered by YOLOv11 · BEVFormer · BEVFusion · Ultra-Fast Lane · Depth Anything V2
Vishal Bansal | Krish Manwani
Datasets: KITTI · nuScenes Training: HPC Cluster · SLURM · PyTorch DDP

## Slide 2
Problem Statement & Research Gaps
The Challenge
1
Detect vehicles, pedestrians, cyclists in real-time across all conditions
2
Identify road lanes to maintain lane discipline
3
Estimate distance to obstacles from a single camera (monocular depth)
4
Predict collision risk before it occurs
5
All tasks must run simultaneously in one system
Gaps in Existing Literature
G1
No unified pipeline — all 15 papers solve tasks in isolation
G2
16-point NDS gap: camera-only (56.9) vs LiDAR+camera (72.9)
G3
Depth + tracking never combined for Time-to-Collision estimation
G4
Grounding DINO never benchmarked on driving datasets
G5
No joint ADAS evaluation metric across tasks
2 / 8

## Slide 3
Literature Review
15 papers · CVPR · ECCV · ICCV · NeurIPS · ICRA · IEEE TPAMI · CoRL (2018–2024)
#
Authors / Paper
Venue
Model
Key Result
Limitation
01
Li et al. · BEVFormer
ECCV 2022
BEVFormer
56.9 NDS · 46.0 mAP (nuScenes)
Camera-only; low-light degradation
02
Liu et al. · BEVFusion
ICRA 2023
BEVFusion
72.9 NDS · 70.2 mAP (nuScenes)
Needs LiDAR + calibration
03
Zhang et al. · ByteTrack
ECCV 2022
ByteTrack
80.3 MOTA · 77.3 IDF1 (MOT17)
No ReID; dense crowd issues
04
Lin et al. · Sparse4D v3
arXiv 2023
Sparse4D v3
56.1 NDS · 49.0 AMOTA
High training cost
05
Wang et al. · StreamPETR
ICCV 2023
StreamPETR
67.6 NDS · 65.3 AMOTA
Latency from temporal dep.
06
Zhao et al. · RT-DETR
CVPR 2024
RT-DETR
53.1 AP @ 108 FPS (COCO)
Higher memory than YOLO
07
Wang et al. · YOLOv10
NeurIPS 2024
YOLOv10
46.3 AP · 25% fewer params
NMS-free optimization complex
08
Ultralytics · YOLOv11
2024
YOLOv11
54.7 mAP(x) · 22% fewer params
No peer-reviewed publication
09
Zheng et al. · CLRNet
CVPR 2022
CLRNet
80.47 F1 (CULane)
Struggles with extreme curves
10
Qin et al. · UFLDv2
TPAMI 2022
UFLDv2
96.4 Acc · 300+ FPS (TuSimple)
Fixed grid; extreme angles
11
Yang et al. · Depth Anything V2
NeurIPS 2024
Depth Anything V2
SOTA NYUv2 & KITTI · 10× faster
Night / tunnel drops
12
Lang et al. · PointPillars
CVPR 2019
PointPillars
82.58 AP Car @ 62 Hz (KITTI)
Loses vertical spatial info
13
Zhou & Tuzel · VoxelNet
CVPR 2018
VoxelNet
SOTA KITTI (2018)
Memory-intensive; not real-time
14
Wang et al. · DETR3D
CoRL 2022
DETR3D
42.5 NDS · 34.6 mAP
No temporal modeling
15
Liu et al. · Grounding DINO
ECCV 2024
Grounding DINO
52.5 AP zero-shot (COCO)
Never tested on driving data
3 / 8

## Slide 4
Proposed Architecture
Unified real-time perception pipeline — camera-first, HPC-trained
INPUT
Camera / Video
YOLOv11
Object Detection
2D Boxes + Classes
Ultra-Fast
Lane v2
Lane Detection
F1 > 96%
Depth
Anything V2
Monocular Depth
Metric Distance
ByteTrack
Multi-Object
Tracking + Velocity
TTC
Calculator
Collision Risk
Time-to-Collision
OUTPUT — Annotated frame: Bounding Boxes · Track IDs · Lane Overlay · Depth Map · TTC Value
Export: ONNX · TensorRT (3–5× faster) · CoreML · OpenVINO
Parallel 3D Branch: BEVFormer (camera-only, NDS 56.9) and BEVFusion (LiDAR+camera, NDS 72.9) trained on HPC cluster via SLURM
4 / 8

## Slide 5
Tech Stack & Datasets
Technology Stack
Detection
YOLOv11 · YOLOv10 · RT-DETR · Grounding DINO
3D / BEV
BEVFormer · BEVFusion · Sparse4D v3 · StreamPETR
Lane & Depth
Ultra-Fast Lane v2 · CLRNet · Depth Anything V2
Tracking
ByteTrack · BotSort · Simple IoU Tracker
Frameworks
PyTorch · MMDetection3D · Ultralytics · Albumentations
Deploy
ONNX · TensorRT · CoreML · OpenVINO · TensorBoard
Datasets
KITTI
2D + 3D detection
7,481 frames · 8 classes · stereo + LiDAR
nuScenes
3D BEV detection
28k frames · 10 classes · 6 cams + LiDAR
TuSimple
Lane detection
3,626 train clips · 96.4% UFLD accuracy
CULane
Lane detection
88k train frames · urban & highway scenes
5 / 8

## Slide 6
Training Strategy & Expected Results
HPC Distributed Training (SLURM + PyTorch DDP)
Nodes / GPUs
4 nodes × 8 GPUs = 32 GPUs total
Framework
torchrun + NCCL all-reduce
Effective batch
batch_per_gpu × 32
Precision
Mixed precision AMP (~2× speedup)
LR scaling
Linear warmup with batch size
Monitoring
TensorBoard · WandB
Performance Targets
YOLOv11 (KITTI)
mAP@0.5 ≥ 85%
YOLOv11 (nuScenes)
mAP@0.5 ≥ 60%
BEVFormer
NDS ≥ 50%
BEVFusion
NDS ≥ 70%
UFLDv2 (TuSimple)
Accuracy ≥ 96%
TTC System
Latency < 50 ms (RTX 3090)
6 / 8

## Slide 7
Contributions
What our work contributes to the field
Unified 5-Task Pipeline
First open-source system combining object detection + lane detection + depth estimation + tracking + TTC in one inference graph.
Novel TTC Estimation (Closes G3)
First integration of ByteTrack per-object velocity with Depth Anything V2 metric depth for real-time Time-to-Collision prediction.
Open-Vocabulary on Driving Data (Closes G4)
First benchmark evaluation of Grounding DINO on KITTI and nuScenes — establishing a zero-shot baseline for autonomous driving.
Camera vs Fusion Study (Closes G2)
Controlled comparison of BEVFormer (camera-only) vs BEVFusion (LiDAR+camera) under identical HPC training conditions.
HPC-Ready Codebase (Closes G1)
Full pipeline with SLURM scripts, DDP training, ONNX/TensorRT export and MMDetection3D integration — open source.
7 / 8

## Slide 8
Thank You
Questions & Discussion
Vishal Bansal | Krish Manwani
IBM Internship Project · 2026
Papers: BEVFormer (ECCV'22) · BEVFusion (ICRA'23) · Sparse4D v3 · StreamPETR (ICCV'23) · RT-DETR (CVPR'24) · YOLOv10/11 · CLRNet (CVPR'22) · UFLDv2 (TPAMI'22) · Depth Anything V2 (NeurIPS'24) · PointPillars (CVPR'19) · VoxelNet (CVPR'18) · DETR3D (CoRL'22) · Grounding DINO (ECCV'24) · ByteTrack (ECCV'22)
Datasets: KITTI · nuScenes · TuSimple · CULane