## Slide 1
IBM INTERNSHIP · RESEARCH PROJECT · 2024
Autonomous Vehicle & Object Detection System
A Unified Real-Time Perception Pipeline
Object Detection · 3D BEV Perception · Lane Detection · Depth Estimation · Collision Avoidance
Powered by YOLOv11 · BEVFormer · BEVFusion · Ultra-Fast Lane · Depth Anything V2 · ByteTrack
Datasets: KITTI · nuScenes
Training: HPC Cluster · SLURM · PyTorch DDP

## Slide 2
OVERVIEW
Agenda
01
Problem Statement
What is the core challenge in autonomous driving perception?
02
Literature Review
15 high-impact papers: object detection, 3D BEV, lane, tracking
03
Research Gaps
Critical gaps identified from surveyed literature
04
Proposed Architecture
Our unified 5-task real-time perception pipeline
05
Tech Stack & Datasets
Models, frameworks, KITTI & nuScenes
06
HPC Training Strategy
Distributed training, SLURM, PyTorch DDP
07
Contributions & Impact
How our work advances the state of the art
2 / 14

## Slide 3
PROBLEM STATEMENT
What Problem Are We Solving?
THE CHALLENGE
— Vehicles, pedestrians, cyclists must be detected in real-time across all weather conditions and lighting scenarios
— Road lanes must be identified to keep the vehicle in lane
— Distance to surrounding objects must be estimated from a single camera (no LiDAR dependency)
— Collision risk must be predicted before it happens
— All of this must run simultaneously, in one system, in real-time
THE GAP IN EXISTING WORK
❶
Papers solve each task in isolation
❷
No unified real-time pipeline exists
❸
Depth & tracking never combined for collision estimation
❹
Open-vocab detection never tested on driving benchmarks
❺
No joint evaluation metric for ADAS
3 / 14

## Slide 4
LITERATURE REVIEW
Survey of 15 High-Impact Papers
Spanning CVPR · ECCV · ICCV · NeurIPS · ICRA · IEEE TPAMI · CoRL (2018–2024)
5 papers
Object Detection
YOLOv11, YOLOv10 RT-DETR Grounding DINO
5 papers
3D / BEV Perception
BEVFormer, BEVFusion Sparse4D v3, StreamPETR DETR3D
2 papers
LiDAR Encoding
PointPillars VoxelNet
3 papers
Lane & Depth
CLRNet UFLD v2 Depth Anything V2
1 paper
Multi-Object Tracking
ByteTrack
Key Venues
CVPR · ECCV · ICCV · NeurIPS · ICRA · IEEE TPAMI · CoRL · arXiv
4 / 14

## Slide 5
LITERATURE REVIEW
Papers 01–08: Detection, BEV & Tracking
#
Authors / Title
Venue
Model
Results
Limitation
01
Li et al.
BEVFormer
ECCV 2022
BEVFormer
56.9% NDS · 46.0% mAP (nuScenes)
Camera-only; degrades in low light
02
Liu et al.
BEVFusion
ICRA 2023
BEVFusion
72.9% NDS · 70.2% mAP (nuScenes)
Needs LiDAR + Camera; calibration sensitive
03
Zhang et al.
ByteTrack
ECCV 2022
ByteTrack
80.3 MOTA · 77.3 IDF1 (MOT17)
No ReID; struggles in extreme crowds
04
Lin et al.
Sparse4D v3
arXiv 2023
Sparse4D v3
56.1% NDS · 49.0% AMOTA (nuScenes)
Complex pipeline; high training cost
05
Zhao et al.
RT-DETR
CVPR 2024
RT-DETR
53.1% AP @ 108 FPS (COCO)
Higher memory than YOLO during training
06
Wang et al.
YOLOv10
NeurIPS 2024
YOLOv10
46.3% AP · 25% fewer params vs YOLOv9
NMS-free adds optimization complexity
07
Ultralytics
YOLOv11
2024
YOLOv11
54.7% mAP (x) · 22% fewer params
No peer-reviewed publication
08
Wang et al.
StreamPETR
ICCV 2023
StreamPETR
67.6% NDS · 65.3% AMOTA (nuScenes)
Temporal dependency increases latency
5 / 14

## Slide 6
LITERATURE REVIEW
Papers 09–15: Lane, Depth, LiDAR & Open-Vocabulary
#
Authors / Title
Venue
Model
Results
Limitation
09
Zheng et al.
CLRNet
CVPR 2022
CLRNet
80.47% F1 (CULane) 97.89% (TuSimple)
Larger model; struggles with extreme curves
10
Qin et al.
UFLDv2
IEEE TPAMI 2022
UFLDv2
96.4% Acc · 300+ FPS (TuSimple)
Fixed grid; misses extreme-angle lanes
11
Yang et al.
Depth Anything V2
NeurIPS 2024
Depth Anything V2
SOTA NYUv2 & KITTI 10× faster vs diffusion
Night / tunnel performance drops
12
Lang et al.
PointPillars
CVPR 2019
PointPillars
82.58% AP Car (KITTI Mod.) @ 62 Hz
Loses fine-grained vertical spatial info
13
Zhou & Tuzel
VoxelNet
CVPR 2018
VoxelNet
SOTA KITTI (2018) All 3 classes
Memory-intensive; not real-time (2018)
14
Wang et al.
DETR3D
CoRL 2022
DETR3D
42.5% NDS · 34.6% mAP (nuScenes val)
No temporal modeling; single frame only
15
Liu et al.
Grounding DINO
ECCV 2024
Grounding DINO
52.5% AP zero-shot (COCO)
Never tested on driving benchmarks
6 / 14

## Slide 7
RESEARCH GAPS
What the Literature Leaves Unsolved
Critical gaps identified across 15 surveyed papers
CRITICAL
G1
No Unified Pipeline
All 15 papers solve tasks in isolation. No open-source system combines detection + lane + depth + tracking + collision in real-time.
CRITICAL
G2
16-Point Camera vs LiDAR Gap
BEVFormer (camera) scores 56.9 NDS vs BEVFusion (LiDAR+cam) at 72.9 NDS. This gap has persisted since 2022 with no clear solution.
CRITICAL
G3
Depth + Tracking Never Fused for TTC
Depth Anything V2 and ByteTrack are studied separately. No paper combines them for Time-to-Collision collision warning.
MODERATE
G4
Grounding DINO Untested on Driving Data
Paper 15 evaluates only on COCO/LVIS. Zero-shot performance on KITTI and nuScenes has never been measured.
MODERATE
G5
No Joint ADAS Evaluation Metric
COCO, CULane, MOT17 are all separate benchmarks. No paper proposes a unified driving perception score.
7 / 14

## Slide 8
PROPOSED SOLUTION
Unified Real-Time Perception Pipeline
Five SOTA models connected into one inference graph — camera-first, HPC-trained
📷
INPUT SOURCE
Camera Video / Image
→
🎯
YOLOv11
Object Detection 2D Boxes + Classes
→
🛣️
Ultra-Fast Lane v2
Lane Detection F1 > 96%
→
📏
Depth Anything V2
Monocular Depth Metric Distance
→
🔄
ByteTrack
Multi-Object Tracking + Velocity
→
⚠️
TTC Calculator
Collision Risk Time-to-Collision
OUTPUT — Single annotated frame: Bounding Boxes · Track IDs · Lane Overlay · Depth Heatmap · ⚠ Collision Warning
Export: ONNX · TensorRT (3–5× faster) · CoreML · OpenVINO
Training: BEVFormer (camera-only 3D) and BEVFusion (LiDAR+Camera 3D) run in parallel track on HPC
8 / 14

## Slide 9
TECH STACK
Models, Frameworks & Tools
Detection
· YOLOv11 (2D, real-time)
· YOLOv10 (NMS-free)
· RT-DETR (transformer)
· Grounding DINO (open-vocab)
3D / BEV
· BEVFormer (camera-only)
· BEVFusion (LiDAR+cam)
· Sparse4D v3 (temporal)
· StreamPETR (online)
Lane & Depth
· Ultra-Fast Lane v2
· CLRNet
· Depth Anything V2
· Metric depth (absolute)
Tracking
· ByteTrack (primary)
· BotSort (ReID-enhanced)
· Simple IoU Tracker (baseline)
Frameworks
· PyTorch + TorchVision
· Ultralytics Ecosystem
· MMDetection3D
· Albumentations
Infra / Deploy
· HPC + SLURM + DDP
· Mixed Precision (AMP)
· ONNX / TensorRT
· TensorBoard / WandB
9 / 14

## Slide 10
DATASETS
Benchmarks Used for Training & Evaluation
KITTI
2D & 3D Object Detection
Classes
8 — Car, Van, Truck, Pedestrian, Cyclist, Tram, Misc
Samples
7,481 training / 7,518 testing frames
Sensors
Stereo camera + 64-beam Velodyne LiDAR
Metric
AP at 0.5/0.7 IoU (Easy / Moderate / Hard)
Source
cvlibs.net/datasets/kitti
nuScenes
Multi-Camera 3D Detection & Tracking
Classes
10 — Car, Truck, Bus, Pedestrian, Cyclist, Motorcycle + more
Samples
700 train / 150 val scenes (28k frames)
Sensors
6 cameras + 1 LiDAR + 5 radars, 360°
Metric
NDS (nuScenes Detection Score), mAP, AMOTA
Source
nuscenes.org
TuSimple & CULane
Lane Detection Benchmarks
TuSimple
3,626 train / 2,782 test clips, 96.4% UFLD Acc
CULane
88k train / 34k test frames, Challenging urban scenes
Metric
F1@50 IoU (CULane), Accuracy (TuSimple)
Source
github.com/TuSimple/tusimple-benchmark
10 / 14

## Slide 11
TRAINING STRATEGY
High Performance Computing — Distributed Training
PyTorch Distributed Data Parallel (DDP)
· Each GPU holds a complete model copy
· Forward + backward run independently per GPU
· Gradients synchronized via NCCL all-reduce
· Effective batch = batch_per_gpu × num_gpus
· LR scaled linearly with effective batch size
· Mixed precision (AMP) gives ~2× speedup
SLURM Job Configuration
#SBATCH --nodes=4
#SBATCH --gres=gpu:8
#SBATCH --time=48:00:00
torchrun \
--nproc_per_node=8 \
--nnodes=4 \
--rdzv_backend=c10d \
training/train_ddp.py \
--config configs/yolo11.yaml
11 / 14

## Slide 12
CONTRIBUTIONS
What Our Work Contributes to the Field
✓
Unified 5-Task Pipeline
First open-source system combining object detection + lane detection + depth estimation + multi-object tracking + collision warning into one real-time HPC-trainable pipeline
✓
Novel TTC Estimation (Closes Gap G3)
First integration of ByteTrack per-object velocity with Depth Anything V2 metric depth for real-time Time-to-Collision estimation from a single monocular camera
✓
Open-Vocab on Driving Data (Closes Gap G4)
First evaluation of Grounding DINO on KITTI and nuScenes — establishing a zero-shot baseline against fine-tuned YOLOv11 on driving benchmarks
✓
Camera vs Fusion Comparison (Closes Gap G2)
Controlled comparison of BEVFormer (camera-only) vs BEVFusion (LiDAR+camera) under identical training settings to quantify the sensor fusion benefit
✓
HPC-Ready Open Codebase
Full pipeline with SLURM scripts, DDP training, ONNX/TensorRT export and MMDetection3D integration — reproducible on any HPC cluster
12 / 14

## Slide 13
EXPECTED RESULTS
Performance Targets & Evaluation Plan
YOLOv11 (KITTI)
mAP@0.5
≥ 85%
2D Object Detection
YOLOv11 (nuScenes)
mAP@0.5
≥ 60%
10-class vehicle detection
BEVFormer (nuScenes)
NDS
≥ 50%
Camera-only 3D detection
BEVFusion (nuScenes)
NDS
≥ 70%
LiDAR+Camera fusion
UFLDv2 (TuSimple)
Accuracy
≥ 96%
Lane detection
TTC System (combined)
Latency
< 50 ms
Real-time on RTX 3090
13 / 14

## Slide 14
Thank You
Autonomous Vehicle & Object Detection System
BEVFormer (ECCV 2022) · BEVFusion (ICRA 2023) · Sparse4D v3 (arXiv 2023) · ByteTrack (ECCV 2022)
CLRNet (CVPR 2022) · UFLDv2 (TPAMI 2022) · Depth Anything V2 (NeurIPS 2024)
RT-DETR (CVPR 2024) · YOLOv10 (NeurIPS 2024) · YOLOv11 (Ultralytics 2024)
PointPillars (CVPR 2019) · VoxelNet (CVPR 2018) · DETR3D (CoRL 2022) · Grounding DINO (ECCV 2024) · StreamPETR (ICCV 2023)
Datasets: KITTI · nuScenes · TuSimple · CULane
Training Infrastructure: HPC Cluster · SLURM · PyTorch DDP · Mixed Precision AMP
14 / 14